## Slide 1
Chapter 2
Electronic
Fundamentals
Voltage • Current • Resistance • Drift Velocity
Sources of Electricity • Materials
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 2
Chapter 2 | Electronic Fundamentals
Voltage (V)
Definition and Key Points
What is Voltage?
Voltage is the expression of potential difference between two points within an electric field.
Key Points:
Denoted by symbol 'V'
Its SI unit is Volt
It represents the energy per unit charge
⚡ Voltage Concept
Point A
(High V)
Point B
(Low V)
← Potential Difference →
V = W / Q
W = Work done, Q = Charge
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 3
Chapter 2 | Electronic Fundamentals
Current (I)
Rate of Flow of Electric Charge
What is Electric Current?
An electric current is the rate of flow of electric charge. These charges can be electrons, ions, and plasma (ionized gases).
Symbol: 'I'
Unit: Ampere (A)
Formula:
I = q / t
I = Current (A) | q = Charge (C) | t = Time (s)
🔌 Conductor Model
electrons (e⁻) → → → →
← Current (I) direction
Types of Charge Carriers:
• Electrons (in conductors)
• Ions (in solutions)
• Plasma (ionized gases)
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 4
Chapter 2 | Electronic Fundamentals
Resistance (R)
Opposition to Electric Current
Definition
Property of a resistor that gives the measurement of difficulty to pass electric current through it.
SI Unit
Ohm (Ω)
Named after German physicist Georg Simon Ohm.
Also Defined As
Ratio of voltage provided to the current flowing through it.
R = V / I
R = V / I
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 5
Chapter 2 | Electronic Fundamentals
Resistor & Use of Resistors
Components and Applications
What is a Resistor?
A resistor is a substance that reduces or limits the current passing through it.
┤▓▓▓▓▓├ Resistor Symbol (—[ R ]—)
Opposition to current flow
Advantages / Uses of Resistor:
🔒 Safety Component
Used as safety component (e.g., Fuse) in circuits
⚡ Limits Current & Voltage
Limits the current and voltage in the circuit
➗ Divider
Used as current divider and voltage divider in circuits
🔌 Power Supply
Delivers constant and desirable power in power supplies
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 6
Chapter 2 | Electronic Fundamentals
Movement of Electrons & Drift Velocity
How current flows in a conductor
Random Motion (No potential applied):
Every material is made of atoms with electrons. These electrons move randomly around the nucleus, so average velocity = zero.
Drift Motion (Potential applied):
When potential difference is applied, electrons orient in the same direction and gain a certain velocity called Drift Velocity.
Every current in a conductor is due to Drift Current.
Drift Current: I = n·e·v·A
🔬 Drift Velocity
Without Voltage:
e⁻→ ←e⁻ e⁻↓ ↑e⁻ →e⁻
With Voltage (Battery):
→e⁻ →e⁻ →e⁻ →e⁻ →e⁻
⊖ Battery ⊕
Formula Derivation:
F = eE (force on electron)
a = eE/m (acceleration)
v = (eE/m)×t (drift velocity)
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 7
Chapter 2 | Electronic Fundamentals
Mobility of Electrons & Current Formula
Key derived quantities
Mobility of Electrons (μe)
The term eE/m is called Mobility of Electrons (μe).
It measures how easily electrons move through a conductor under an electric field.
Unit: m²/V·sec (m² per Volt per second)
⚠️ Important Fact
Drift velocity of electrons is very small (range: 0.1 mm/s). At this velocity, it takes almost 17 minutes for one electron to pass through 1m of conducting wire!
📐 Formulas
Drift Velocity:
v = (eE/m) × t
Mobility:
μe = eE/m
Current (Drift):
I = n·e·v·A
Where: n=no. of electrons, e=electron charge,
v=drift velocity, A=cross-sectional area
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 8
Chapter 2 | Electronic Fundamentals
Sources of Electricity
Five Major Sources
💧
Hydro Power
Electricity from flowing water via turbines & generators
⚛️
Nuclear Energy
Fission & Fusion reactions release massive energy
☀️
Solar Energy
Photovoltaic cells convert sunlight to electricity
🌬️
Wind Energy
Wind turbines convert wind energy to electrical energy
🌡️
Thermal Energy
Converting heat energy into electrical energy (Seebeck effect)
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 9
Chapter 2 | Electronic Fundamentals
1. Hydro Power
Most Used Electricity Source in Nepal
• Hydropower is electricity produced from generators driven by turbines that convert potential energy into kinetic energy.
• Water is stored at higher elevation, then led downwards through large pipes or tunnels (Penstocks) to lower elevation.
• The difference in elevation is called Head.
• Falling water hits the turbine → Turbine rotates → Generator converts mechanical energy into electrical energy.
• Transformers are then used to convert the voltage for transmission.
⚡ How it Works
💧 Reservoir
(High Elevation)
↓ Penstock
(Pipe)
🔄 Turbine
(Rotates)
⚙️ Generator
(Mech→Elect)
🔌 Transformer
(Voltage↑)
EMF = BlvSinθ
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 10
Chapter 2 | Electronic Fundamentals
2. Nuclear Energy
Fusion & Fission
⚡ Nuclear Fusion
Two or more small/light nuclei collide with each other to form a heavier nucleus.
Occurs in the Sun where hydrogen isotopes combine under high pressure and temperature.
Reaction:
₁H² + ₁H³ → ₂He⁴ + ₀n¹ + 18 MeV
(Deuterium + Tritium → Helium + Neutron + Energy)
💥 Nuclear Fission
Nucleus of a large atom is bombarded with low energy neutrons. It splits into smaller nuclei releasing large amounts of energy.
Used in nuclear power reactors (easy to control and produce large energy).
Reaction:
₉₂U²³⁵ + ₀n¹ → ₃₆Kr⁸⁹ + ₅₆Ba¹⁴⁴ + 3₀n¹ + 200 MeV
(Uranium bombarded → Krypton + Barium + Neutrons + Energy)
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 11
Chapter 2 | Electronic Fundamentals
3. Solar Energy
Photovoltaic Effect
• Solar technology converts light energy into electrical energy through photovoltaic panels or concentration of solar radiation.
• Photovoltaic cells (solar cells) generate a small electric voltage when light strikes them — called Photovoltaic Effect.
• Photovoltaic cell consists of two types of semi-conductors placed between metallic plates connected to batteries/load.
• n-type (negatively charged) and p-type (positively charged) semi-conductors are used.
• Power generated by a single solar cell is only 2 Watts.
• Solar panels are faced towards South for maximum sunlight. They should be cleaned regularly for maximum efficiency.
☀️ Photovoltaic Cell
n-type (⊖ ⊖ ⊖ ⊖ ⊖)
p-type (⊕ ⊕ ⊕ ⊕ ⊕)
↕ Junction
Light →
(Photons)
→ Load /
Battery
Photo-electric Effect
Electrons emitted → Current flows
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 12
Chapter 2 | Electronic Fundamentals
4. Wind Energy & 5. Thermal Energy
Converting Natural Energy to Electricity
🌬️ Wind Energy
• Uses aerodynamic force to form the rotor blade to rotate wind turbine.
• Wind turbine converts wind energy to electrical energy.
• Rotor is connected to generator through gearbox and brakes which helps generate consistent turbine rotation even in different wind speeds.
• Generator converts mechanical energy into electrical energy.
🌡️ Thermal Energy
• Process of converting heat energy into electrical energy.
• A temperature difference between two dissimilar electrical conductors or semi-conductors produces voltage difference between the two substances.
• This is also known as the Seebeck Effect.
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 13
Chapter 2 | Electronic Fundamentals
Flow of Current
Conventional vs Modern Flow
Electric circuit is a closed path which has potential difference generated and have electronic load (bulb, fan, etc.) and switch.
① Conventional Flow
Battery
⊕ ⊖
→ I
Load
—[R]—
• Positive charges flow from +ve to -ve terminal.
• This is the world standard followed everywhere.
• Electronic circuits produce results independent of current — that is why this flow is still in use.
② Modern Flow
Battery
⊕ ⊖
← e⁻
Load
—[R]—
• Electrons actually flow from -ve to +ve potential through the circuit.
• Such type of flow of current is called Modern Flow of Current.
• Mobility of proton is less than electron.
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 14
Chapter 2 | Electronic Fundamentals
Factors Affecting Resistance (R)
4 Key Factors
1
Length of Conductor (l)
Resistance is directly proportional to length.
Longer wire → Greater Resistance
Shorter wire → Lesser Resistance
R ∝ l
2
Thickness / Cross-Section Area (A)
Resistance is inversely proportional to cross-sectional area.
Thicker wire → Less Resistance
R ∝ 1/A
3
Material Used
Resistance depends on type of substance used.
Metals have low resistance compared to non-metals & metalloids.
R = ρl/A
4
Temperature
Resistance increases with increase in temperature for most conductors.
This is called Positive Temperature Coefficient.
R ↑ as T ↑
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 15
Chapter 2 | Electronic Fundamentals
Resistivity (ρ) & Formula
Combining All Factors
Combining both proportionalities:
R ∝ l/A → R = ρl/A
Where ρ (rho) is Resistivity — property of resistance that limits current.
Unit of ρ: Ω·m (Ohm-meter)
Example 1: Copper Wire
Given: l = 5m, A = 0.01m², ρ = 1.72×10⁻⁸ Ω·m
R = (1.72×10⁻⁸ × 5) / 0.01
= 8.6×10⁻⁶ Ω
∴ R = 8.6×10⁻⁶ Ω
Example 2: Silver Wire
Given: l = 8m, A = 0.01mm² = 10⁻⁸m², ρ = 1.59×10⁻⁸ Ω·m
R = (1.59×10⁻⁸ × 8) / 10⁻⁸
= 12.72 Ω
∴ R = 12.72 Ω
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 16
Chapter 2 | Electronic Fundamentals
More Numerical Problems
Resistance Calculations
Iron Wire — Length 1.5km
Given: l=1500m, A=0.01cm²=10⁻⁶m², ρ=10⁻⁷Ω·m
R = 10⁻⁷×1500/10⁻⁶ = 1500×10⁻¹ = 150Ω
∴ R = 150 Ω
Copper Wire — Find Length
Given: A=10⁻³cm²=10⁻⁷m², R=15Ω, ρ=1.72×10⁻⁸Ω·m
l = RA/ρ = 15×10⁻⁷/(1.72×10⁻⁸)
= 87.20m
∴ l = 87.20 m
Silver Wire — Radius 0.7mm
Given: l=0.5m, r=0.7mm=7×10⁻⁴m, ρ=1.59×10⁻⁸Ω·m
A=πr²=154×10⁻⁸m²
R = 1.59×10⁻⁸×0.5/(154×10⁻⁸)
= 5.162×10⁻³Ω
∴ R = 5.162×10⁻³ Ω
Wire Cut at Half Point
Given: Length halved: l₂ = l₁/2, Area same
R₂ = ρl₂/A = ρ(l₁/2)/A = ½ × R₁
∴ R₂ = R₁/2 (Halved)
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 17
Chapter 2 | Electronic Fundamentals
Classification of Materials
Based on Resistance: Conductor, Semiconductor, Insulator
🚫 Insulator
Does NOT allow electric current to flow easily.
Electrons require very high energy to enter conduction band.
Valence band & conduction band have MAXIMUM gap.
Examples: Plastic, Wood, Rubber, Glass
Band Gap: MAX
✅ Conductor
Allows electric current to flow very easily.
Large number of free electrons present.
Valence and conduction band are OVERLAPPED.
Examples: Copper, Iron, Silver, Gold, Aluminium
Band Gap: ZERO (Overlapped)
⚡ Semi-conductor
Conductivity between insulator and conductor.
Conductivity can be increased by DOPING (adding impurities like Al, Boron).
Minimum electric gap between bands.
Examples: Metalloids — Silicon, Carbon
Band Gap: MINIMUM
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 18
Chapter 2 | Electronic Fundamentals
Resistance vs Resistivity & Conductance
Comparison and Related Concepts
S.N. | Resistance (R) | Resistivity (ρ)
i) | Measurement of difficulty of passing electric current through material. | Property of material that determines the resistance of substances having unit length and unit area.
ii) | Unit: Ohm (Ω) | Unit: Ohm-meter (Ω·m)
iii) | Depends on length, area, material, temperature. | Depends only on material (intrinsic property).
Conductance
It is the measurement of easiness of passing electric current through the material.
Unit: ℧ / mho / Siemen (S) | Conductance = 1/R
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor

## Slide 19
Chapter 2 — Key Formulas Summary
Voltage
V = W/Q
Unit: Volt (V)
Current
I = q/t
Unit: Ampere (A)
Resistance
R = V/I
Unit: Ohm (Ω)
Resistivity
R = ρl/A
Unit: Ω·m
Drift Velocity
v = (eE/m)·t
Unit: m/s
Drift Current
I = n·e·v·A
Unit: Ampere (A)
Prepared by: Hikmat Shahi Thakuri | Assistant Computer Instructor